CITY OF IRVINE

STANDARD RESIDENTIAL SECURITY CODE PROVISIONS

[Version 2.0  12/08]

This document shall be completed by the design professional of record. The completed document shall be incorporated, in its entirety, along with the City of Irvine Standard Security Code Plan Requirements and Definitions into the plans submitted for approval prior to permit issuance.

INSTRUCTION: Those provisions preceded by an asterisk (*) shall be completed if applicable and an “A” shall be inserted in the space preceding the provision; if not applicable, an “N/A” shall be inserted.

Those provisions preceded by a [P] shall be depicted in the plans via notes, details, plan and/or elevation views in a manner that clearly demonstrates compliance to the requirement. Such depictions shall be crossed referenced within the brackets { } provided or note shall be completed as otherwise instructed.

KEYING REQUIREMENTS [Adapted from IMC Sec. 5-9-511]

Upon occupancy by the owner or proprietor, each single unit shall have locks using combinations which are interchange free from locks used in all other separate dwellings, proprietorships or similar distinct occupancies.

FRAMES; JAMBS; STRIKES; HINGES [Adapted from IMC Sec. 5-9-513]

Installation and construction of frames, jambs, strikes and hinges for exterior swinging doors and door leading from garage into dwelling unit shall be as follows:

A.	Door jambs shall be installed with solid backing in such a manner that no voids exist between the strike side of the jamb and the frame opening for a vertical distance of six inches each side of the strike.

B.	In wood framing, horizontal blocking shall be placed between studs at door lock height for three stud spaces each side of the door openings. Trimmers shall be full length from the header to the floor with solid backing against sole plates.

C.	Door stops on wooden jambs for in-swinging doors shall be of one-piece construction with the jamb. Jambs for all doors shall be constructed or protected so as to prevent violation of the strike.

D.	The strike plate for deadbolts on all wood framed doors shall be constructed of minimum 16 U.S. gauge steel, bronze, or brass, and secured to the jamb by a minimum of two screws, which must penetrate at least two inches into solid backing beyond the surface to which the strike is attached.

E.	Hinges for out-swinging doors shall be equipped with non-removable hinge pins or a mechanical interlock to preclude removal of the door from the exterior by removing the hinge pins.

F.	When pairs of doors are utilized in residential structures, a one-piece assembly attached to the full-length edge of the inactive door leaf, incorporating an astragal and flush-bolts for the header and threshold, will be accepted as a strike plate, provided the assembly is constructed of aluminum or steel a minimum of one-eighth inch in thickness.

G.	All exterior doors equipped with lever-handled locking devices which operate the deadbolt shall have thresholds designed and installed so as to prevent the passing of rigid materials between the door and threshold to the interior.

(*)  || STANDARDS FOR LOUVERED WINDOWS [Ref. IMC Sec. 5-9-514]

[P] Louvered windows shall not be utilized if any portion of it is within eight feet vertically or six feet horizontally from any exterior accessible surface or any adjoining roof, balcony, landing, stair tread, platform or similar structure.

Ref. {Ref. elevation views, window schedule -      }

(*)  || STANDARDS FOR GARAGE DOORS: ROLLING OVERHEAD, SOLID OVERHEAD [Ref. Sec. 5-9-515]

A.	Wood doors shall have panels a minimum of 5/16 inch in thickness with the locking hardware being attached to the support framing.

B.	Aluminum doors shall be a minimum thickness of 0.0215 inches and riveted together a minimum of 18 inches on center along the outside seams. There shall be a full width horizontal beam attached to the main door structure which shall meet the pilot, or pedestrian access, door framing within three inches of the strike area of the pilot or pedestrian access door.

C.	Fiberglass doors shall have panels a minimum density of six ounces per square foot from the bottom of the door to a height of seven feet. Panels above seven feet and panels in residential structures shall have a density not less than five ounces per square foot.

D.	Doors utilizing a cylinder lock shall have a minimum five-pin tumbler operation with the locking bar or bolt extending into the receiving guide a minimum of one inch.

E.	Doors that exceed 16 feet in width shall have two lock receiving points; or, if the door does not exceed 19 feet, a single bolt may be used if placed in the center of the door with the locking point located either at the floor or door frame header; or, torsion spring counterbalance-type hardware may be used.

F.	Except in a residential building, doors secured by electrical operation shall have a keyed-switch to open the door when in a closed position, or by a signal locking device.

G.	Doors with slide bolt assemblies shall have frames a minimum of 0.120 inches in thickness, with a minimum bolt diameter of 1/2 inch and protrude at least one and one-half inches into the receiving guide. A bolt diameter of 3/8 inch may be used in a residential building. The slide bolt shall be attached to the door with non-removable bolts from the outside. Rivets shall not be used to attach slide bolt assemblies.

STANDARDS FOR EXTERIOR DOORS AND OPENININGS [Ref. Sec. 5-9-516]

Except for vehicular access doors, all exterior swinging doors of any residential building and garages, including the door leading from the garage area into the dwelling unit shall be equipped as follows:

A.	[P] All wood doors shall be of solid core construction with a minimum thickness of 1 3/4 inches, or with panels not less than 9/16 inch thick.

Ref. {ref. plans and/or door schedule -       }

B.	A single or double door shall be equipped with a single cylinder deadbolt lock. The bolt shall have a minimum projection of one inch and be constructed so as to repel cutting tool attack. The deadbolt shall have an embedment of at least 3/4 inch into the strike receiving the projected bolt. The cylinder shall have a cylinder guard, a minimum of five-pin tumblers, and shall be connected to the inner portion of the lock by connecting screws of at least one-fourth inch in diameter.

C.	The inactive leaf of double door(s) shall be equipped with metal flush bolts having a minimum embedment of 5/8 inch into the head and threshold of the door frame.

D.	[P] Glazing in exterior doors, or within 40 inches of any locking mechanism, shall be of fully tempered glass or rated burglary resistant glazing.

Ref. {ref. plans and/or window schedule or note: No glazing in exterior doors or within 40 inches of any locking mechanism -       }

E.	Except where clear vision panels are installed, all front exterior doors shall be equipped with a wide-angle (180 degrees) door viewer.

STANDARDS FOR ADDRESSING AND SITE MAPPING [Ref. Sec. 5-9-516]

(*)  || Single-family residential buildings shall display a street address number conforming to the following specifications:

A.	[P] Numerals shall be located where they are clearly visible from the street on which they are addressed. They shall be of a color contrasting to the background to which they are affixed. Method of attachment shall not include the use of two-sided tape or any material not resistant to weather conditions.

Ref.{Ref. elevation views -       }

B.	[P] Numerals shall be no less than four inches in height and illuminated during the hours of darkness. The numerals and light source shall be contained within a single, weather-resistant fixture. The light source shall be provided with an uninterruptible A.C. power source or controlled only by a photoelectric device. Nothing in this section shall preclude the requirement for circuit protection devices where applicable. Ref.{Ref. elevation views and applicable notes and/or details -       }

C.	[P] Address numbers on buildings farther than 100 feet from the center line of the addressed street shall, in addition to the illuminated address fixture, provide highly reflective four-inch high numerals, placed at the driveway entrance, at a height between 24 and 42 inches.

Ref.{Ref. plans, or note: Building addressing less than 100 feet from street c.l. -       }

D.	[P] Any building which affords vehicular access to the rear through a public or private alley shall display, in a clearly visible location, a highly reflective address number a minimum of four inches in height.

Ref.{Ref. elevations or note: This provision not applicable -       }

E.	[P] Second dwelling units on the same single-family parcel, which are further than 100 feet from the center line of the addressed street or are not visible from the addressed street, in addition to the illuminated address fixture, shall have an illuminated address fixture containing a directional arrow or wording indicating the second dwelling unit location, and mounted on the primary dwelling unit that is visible from the addressed street.

Ref.{Ref. plans, elevations, and details or note: This provision not applicable -       }

F.	[P] There shall be positioned, at each entrance of a tract of 20 or more residences constructed on private streets, but using a single public street name and address, an illuminated diagrammatic representation of the complex which depicts the location of the viewer and the unit designations within the complex. It shall be lighted during the hours of darkness utilizing a light source which is constructed of weather and vandal resistant materials and provided with an uninterrupted power source or controlled by a photoelectric device. Nothing in this section shall preclude the requirement for circuit protection devices where applicable.

Ref. {Ref. plans, elevations, and details or note: This provision not applicable -       }

(*)  || Multiple family buildings shall display a street address number conforming to the following specifications:

A.	[P] Each individual unit within the complex shall display a prominent identification number not less than four inches in height, contrasting in color to the background to which it is affixed and clearly visible to approaching vehicles and/or pedestrians. It shall be located near, but not on, the dwelling unit entry door.

Ref. {Ref. elevation views and applicable notes and/or details -       }

B.	[P] Numerals shall be no less than four inches in height and illuminated during the hours of darkness. The numerals and light source shall be contained with a single, weather-resistant fixture. The light source shall be provided with an uninterruptible A.C. power source or controlled only by a photoelectric device. Nothing in this section shall preclude the requirement for circuit protection devices where applicable. An illuminated fixture is not required when the address number can be lighted by an area lighting as required in section 5-9-516E regarding walkways and doors. Ref.{Ref. elevation views and applicable notes and/or details -       }

C.	[P] Complexes with two or more buildings with the same address or buildings containing a minimum of six separate street addresses, shall display minimum six-inch high identification numbers noting the address number and range of unit and/or building numbers within the building. They shall be placed on the building between eight and ten feet from ground level, and visible to approaching vehicles and/or pedestrians from all building sides. Identification numbers shall be of a color contrasting to the background to which they are attached and be illuminated during the hours of darkness. The light source shall be provided with an uninterruptible A.C. power source or controlled only by a photoelectric device.

Ref. {Ref. elevation views and applicable notes and/or details -       }

D.	[P] Driveways servicing more than 20 individual dwelling units shall have minimum four-inch high identification numbers, noting the range of unit numbers, placed at the entrance to each driveway at a height between 36 and 42 inches above grade. The light source shall be provided with an uninterruptible A.C. power source or controlled only by a photoelectric device.

Ref. {Ref. plans, elevations and applicable notes and/or details or note: This provision not applicable -       }

E.	[P] There shall be positioned, at each entrance of a multiple family dwelling complex with more than four buildings, an illuminated diagrammatic representation of the complex, which depicts the location of the viewer and the unit designations within the complex. It shall be lighted during the hours of darkness utilizing a light source, which is constructed of weather and vandal resistant materials and provided with an uninterruptible A.C. power source or controlled by a photoelectric device. Nothing in this section shall preclude the requirement for circuit protection devices where applicable.

Ref. {Ref. plans, elevations and applicable notes and/or details or note: This provision not applicable -       }

F.	[P] In multiple family complexes, garages or carports not directly attached to the dwelling unit or placed next to the dwelling unit and discernible as being associated with one addressed dwelling unit shall not use corresponding dwelling unit addresses to identify the garage or carport.

Ref. {Ref. plans, elevations and applicable notes and/or details or note: This provision not applicable -       }

G.	Address identification numbers and/or letters shall not be affixed to a surface using two-sided tape or any material not resistant to weather conditions.

STANDARDS FOR EXTERIOR LIGHTING STANDARDS [Ref. Sec. 5-9-516]

[Note: Performance standards are contained herein for reference. Compliance shall be demonstrated in photometric study preceding plan check approval.]

(*)  || Single-family dwelling units, garages, and tracts of homes shall conform to the following lighting standards:

A.	[P] All garage doors shall have a light fixture that is capable of illuminating the door. Garage doors accessed from alleys are to have vandal resistant light fixtures.

Ref. {Ref. plans, elevations and applicable notes and/or details or note: This provision is not applicable -       }

B.	Private streets, alleys, and fire department required roadways designed for use only in emergency situations shall be illuminated using the same standards as established for public thoroughfares.

(*)  || Multiple-family buildings, carports, parking areas, driveways, and walking surfaces shall conform to the following lighting standards:

A.	All vehicular drive surfaces, open parking areas and carports shall be illuminated with a minimum maintained one foot-candle of light at ground level during the hours of darkness.

B.	All exterior common area pedestrian walkways and recreation areas shall be illuminated with a minimum maintained 0.25 foot-candle of light at ground level during the hours of darkness.

C.	Open stairways and enclosed common area corridors shall be illuminated with a minimum maintained 0.5 foot-candle of light on all landings and stair treads during the hours of darkness. Enclosed stairways shall be illuminated at all times with a minimum maintained one footcandle of light on all landings and stair treads.

D.	Cluster mailboxes, trash enclosures/areas, vending machines, and public phones located on the exterior shall be illuminated with a minimum maintained one foot-candle of light, measured within a five-foot radius at ground level, during the hours of darkness.

E.	Recessed areas of building or fences, which have a minimum depth of two feet, a minimum height of five feet, and do not exceed six feet in width and are capable of human concealment, shall be illuminated with a minimum maintained 0.25 foot-candles of light at ground level during the hours of darkness. This requirement applies to defined recessed areas which are within six feet of the edge of designated walking surface with an unobstructed pathway to it, not hindered by walls or hedge row landscaping a minimum of two feet in height.

F.	Accessible luminaires utilized to meet the requirements of this section shall have vandal resistant light fixtures and be not less than three feet in height from the walking surface when used to illuminate walkways and a minimum of 78 inches in height above the driving surface when illuminating surfaces associated with vehicles. Light fixtures shall be deemed accessible if mounted within 15 feet vertically or six feet horizontally from any accessible surface or any adjoining roof, balcony, landing, stair tread, platform or similar structure.

G.	The light source utilized to comply with this section to meet parking and drive surface lighting shall have a rated average bulb life of not less than 10,000 hours.

H.	[P] A site plan shall be provided showing buildings, parking area, walkways, detailed landscaping and a point-by-point photometric calculation of the required light levels. Landscaping shall not be planted so as to obscure required light levels. Foot-candles shall be measured on a horizontal plane and conform to a uniformity ratio of four to one (4:1 maximum/minimum). Ref. {Ref. plans -       }

I.	The light source shall be controlled by a photocell device or a timeclock with an astronomic feature.

(*)  || STANDARDS FOR COMMON AREA LAUNDRY ROOMS IN MULTI-FAMILY COMPLEXES [Ref. IMC Sec. 5-9-516]

A.	[P] Entry doors shall have:

1.	A minimum 600 square-inch clear vision panel, in the upper half of the door.

2.	Automatic, hydraulic door closures.

3.	Self-locking door locks equipped with a dead-locking latch, allowing exiting by a single motion and openable from the inside without the use of a key or any special knowledge or effort.

4.	Non-removable hinge pins for out-swinging doors to preclude removal of the door from the exterior by removing the hinge pins.

5.	A latch protector consisting of minimum 0.125-inch-thick steel attached to the door's exterior with non-removable bolts from the exterior. It shall be two inches wide and extend a minimum of five inches above and below the strike opening and extend a minimum of one inch beyond the edge of the door. It shall have a metal anti-spread pin a minimum of 1/2 inch in length.

Ref. {Ref. plans, elevations and applicable notes and/or details -       }

B.	The laundry room shall be illuminated at all times with a minimum maintained five foot-candles of light at floor level, using a non-interruptible power source. There shall be no light switches inside the room that control light fixtures used to meet the lighting requirement.

C.	Any portion of an openable window which is within eight feet vertically or six feet horizontally from any accessible surface or any adjoining roof, balcony, landing, stair tread, platform, or similar surface, or any climbable pole or tree, or any surface providing a foothold, shall be secured as follows:

1.	Windows shall not provide an opening greater than 96 square inches: or

2.	Transom windows opening at the top and hinged at the bottom may be utilized provided the bottom portion is not less than six feet from an exterior accessible surface.

Ref.{Ref. plans, elevations and applicable notes and/or details or note: This provision not applicable -       }

D.	The entire laundry room shall be visible from the exterior along common area walking or driving surfaces. Perimeter windows and interior mirrors may be utilized to meet this requirement.

E.	Laundry rooms are to be located in high activity areas with natural surveillance opportunities, and not in remote or isolated locations.

(*)  || STANDARDS FOR MAILBOXES [Ref. IMC Sec. 5-9-516]

Mail boxes in multi-family complexes are to be located in highly visible areas adjacent to common area activity amenities.

Ref. {Ref. plans -       }

(*)  || EMERGENCY ACCESS [Ref. IMC Sec. 5-9-519]

A.	Private roads and parking areas or structures controlled by unmanned mechanical parking type gates shall provide for police emergency access utilizing an approved key switch device and designed as follows:

1.	A control pedestal consisting of a metal post/pipe shall be installed at a height of 42 inches and a minimum of 15 feet from the entry/exit gate. It shall be located on the driver's side of the road or driveway and accessible in such a manner as to not require a person to exit their vehicle to reach it; nor to require any back-up movements in order to enter/exit the gate.

2.	A control housing consisting of a heavy gauge metal, vandal and weather resistant square or rectangular housing which shall be installed on the top of the control pedestal. Keyswitch is to be mounted on the side facing the roadway.

Ref. {Ref. plans, elevations and applicable notes and/or details or note: These provisions are not applicable -       }

B.	Lockable pedestrian gates to residential recreation areas serving six or more dwelling units, and gates or doors to common walkways or hallways of residential complexes where the there are four or more dwelling units within the complex, shall provide for police emergency access utilizing an approved keyswitch device or approved key vault which shall be installed as follows:

1.	Pedestrian gates/doors using an electromagnetic type lock shall install a keyswitch within a telephone/intercom console or in a control housing as described in section (a)(2) above.

2.	Pedestrian gates/doors utilizing mechanical locks shall install a key vault adjacent to each gate/door, securely attaching it to a fence or wall.

Ref. {Ref. plans, elevations and applicable notes and/or details or note: These provisions are not applicable -       }