CITY OF IRVINE

STANDARD PARKING FACILITY SECURITY CODE PROVISIONS

[Version 1.0 12/08]

This document shall be completed by the design professional of record. The completed document shall be incorporated, in its entirety, along with the City of Irvine Standard Security Code Plan Requirements and Definitions into the plans submitted for approval prior to permit issuance.

INSTRUCTION: Those provisions preceded by an asterisk (*) shall be completed if applicable and an “A” shall be inserted in the space preceding the provision; if not applicable, an “N/A” shall be inserted.

Those provisions preceded by a [P] shall be depicted in the plans via notes, details, plan and/or elevation views in a manner that clearly demonstrates compliance to the requirement. Such depictions shall be crossed referenced within the brackets { } provided or note shall be completed as otherwise instructed.

STANDARDS PARKING FACILITY [Ref. IMC Sec. 5-9-518]

The following standards apply to any structure, garage or covered parking surface intended primarily for the storage of motor vehicles for any period of time.

A.  [P] Remote or detached parking facilities or any other parking surfaces which are constructed as a separate entity shall be assigned a street address number. The numerals shall be displayed at the main entrance using numbers a minimum of eight inches in height and of a color contrasting to the background to which they are affixed. {Ref. plans, elevations and applicable notes and/or details-      }

B.  Restrooms shall not be open to the general public and shall be continuously locked, with access provided only to authorized individuals. They shall be located in an area which is highly visible from the parking attendant kiosk or other area where natural surveillance is afforded.

C.  [P] Directional signage, including floor designation and section, shall be provided on each level to expedite movement within the facility. Signage shall be a minimum of 12 inches in height and of a contrasting color to the background. It shall be displayed not less than 60 inches from the parking surface and be highly visible from within any portion of the facility. {Ref. plans, elevations and applicable notes and/or details-      }

D.  Structures or fencing designed to screen trash enclosures from public view shall be designed with no more than three solid walls and an access gate(s). They shall be designed in such a manner as to allow a maximum of six inches clearance between trash bins, walls and gates.

E.  Bicycle storage units or racks shall be located in high visibility areas.

F.  If removal of a metal drainage grating being used at grade along the exterior of the facility would provide access into the interior, the grating shall be securely fastened, rendering it non-removable from the exterior.

G.  Solid perimeter walls shall be either full height floor to ceiling or not exceed 42 inches in height from the parking surface.

H.  [P] The number of pedestrian and vehicular access points shall be minimized. Except at vehicle and primary pedestrian openings, the structure shall be designed, to the satisfaction of the City, to preclude human entry from any exterior accessible surface to a height of eight feet. Chain link fencing shall not be utilized if visible from a public right of way. When required, fire authority openings in the form of swing-out gates shall be provided and secured by a padlock with a minimum 3/8-inch diameter shackle and five-pin tumbler operation. {Ref. plans, elevations and applicable notes and/or details or note: This provision is not applicable-      }

I.   [P] Exterior pedestrian doors which provide access into the parking facility, shall be constructed and equipped as follows:

1.   A minimum 18 gauge steel and equipped with automatic hydraulic closure

device.

2.   A minimum 100-square-inch vision panel, with the width not less than five inches, to provide visibility into the area being entered. Vision panels shall meet requirements of the Uniform Building Code.

3.   Vision panels shall preclude manipulation of the interior locking device from the exterior.

4.   No openings within twenty-four inches of the locking device which would allow a piece of metal, 1/16-inch diameter or greater to be inserted and access gained to the interior side of the door.

5.   When panic hardware is required, it shall have a self-locking mechanism and be constructed/equipped as follows:

a.   Panic hardware on pairs of doors shall contain a minimum of two locking points on each door; or

b.   On single doors, panic hardware may have one locking point, which is not located at either the top or bottom of the doorframe. When mortise hardware is utilized, a protective astragal consisting of a minimum 0.125 inch thick steel shall be attached to the exterior of the door and rendered nonremovable from the exterior. It shall be two inches wide and extend a minimum of five inches above and below the strike opening and extend a minimum of one inch beyond the edge of the door.

c.   Double doors containing panic hardware shall have an astragal attached to the doors at their meeting point, which will close the opening between them, but not interfere with the operation of either door. Fire rated astragals, meeting specifications of the Building Code, shall be utilized when required. Astragals are not required when panic hardware is utilized with push pads offset a minimum of three inches from the door edges.

{Ref. plans and door schedule or note: This provision is not applicable as no exterior access doors provided.}

6.   [P] Emergency exits not intended, as a primary entrance shall have no exterior handles, knobs, or levers. {Ref. plans, elevations and applicable notes and/or details or note: This provision is not applicable-      }

7.   Hinges shall be equipped with nonremovable hinge pins or a mechanical interlock to preclude removal of the door from the exterior by removing the hinge pins.

J.   Stairways shall be designed as follows:

1.   [P] Interior doors shall have glazing panels a minimum of five inches wide and 20 inches in height and meet requirements of the Building Code. {Ref. plans and door schedule or note: This provision is not applicable as no interior stairway doors provided.-      }

2.   Areas beneath stairways at or below ground level shall be fully enclosed or access to them restricted.

3.  Stairways shall be designed to be completely visible from either the interior or exterior or both, unless mandated by the Building Code to be enclosed.

4.  Fully enclosed interior or exterior stairways with solid walls, when required, shall have shatter resistant mirrors or other equally reflective material at each level and landing and be designed or placed in such a manner as to provide visibility around corners.

K.  Elevator cabs and lobbies shall be designed as follows:

1.   [P] Elevators which serve more than two floors, above ground level, with at least one shaft wall exposed to the exterior or interior shall have clear glazing installed in one wall to provide visibility into the elevator cab. {Ref. plans, elevations and applicable notes and/or details or note: This provision is not applicable -     }

2.   [P] Elevator cabs, the interiors of which are not completely visible when the door is open from a point centered on and 36 inches away from the door, shall have shatter resistant mirrors or other equally reflective material so placed as to make visible the entire elevator cab from this point. The elevator cab shall be illuminated at all times with a minimum maintained two foot-candles of light at floor level. {Ref. plans, elevations and applicable notes and/or details or note: This provision is not applicable as interior is completely visible per specification above}

3.   Elevator emergency stop buttons shall be so installed and connected as to activate the elevator alarm when utilized.

4.   [P] Elevator lobbies, if enclosed, shall be constructed of glazing, the maximum amount allowed by the Building Code. {Ref. plans, elevations and applicable notes and/or details or note: This provision is not applicable as interior is completely visible per specification above-      }

L.   Lighting of driveways, parking areas, walkways and doors shall conform to the following standards and be arranged in such a way so as to conform to Zoning Code Section 3-16-1 which requires that direct rays be confined to the site and that adjoining properties are protected from glare.

1.   All parking, driving, and walking surfaces, except stairways, shall be illuminated at all times with a minimum maintained 1.25 foot-candles of light.

Exception:  Parking facilities which have physically precluded pedestrian and vehicle access during nonbusiness hours may provide a minimum maintained 0.25 of light on the parking, walking and driving surfaces.

2.   Stairways shall be illuminated at all times with a minimum maintained two foot-candles of light on all landings and stair treads.

3.   All types of exterior doors shall be illuminated, during the hours of darkness, with a minimum maintained one foot-candle of light, measured within a five-foot radius of each side of the door at ground level.

4.   Recessed areas of buildings or fences, which have a minimum depth of two feet, a minimum height of five feet, and do not exceed six feet in width and are capable of human concealment, shall be illuminated with a minimum maintained 0.25 foot-candles of light at ground level during the hours of darkness. This requirement applies to defined recessed areas which are within six feet of the edge of a designated walking surface with an unobstructed pathway to it, not hindered by walls or hedge row landscaping a minimum of two feet in height.

5.   All luminaires utilized to meet the requirements of this section shall have vandal resistant light fixtures, if on the exterior, with no portion of the fixture placed less than 72 inches above the walking or driving surface.

6.   The light source utilized to comply with this section to meet parking and drive surface lighting shall have rated average bulb life of not less than 10,000 hours.

7.   [P] See plan sheet <text box> showing buildings, parking area, walkways, detailed landscaping and a point-by-point photometric calculation of the required light levels. Note: Foot-candles are measured on a horizontal plane and conform to a uniformity ratio of 4:1 average/minimum. Landscaping shall be planted and maintained in a manner so as not to obscure required light levels.

8.  The light source shall be controlled by a photocell device or a timeclock with an astronomic feature and capable of operating during a power failure.

M.  Landscaping around the perimeter of the structure shall not provide access to any portion of the structure unless the accessible point is protected as described in subsection H. hereinabove.

(*)  || STANDARDS FOR GARAGE DOORS: ROLLING OVERHEAD, SOLID OVERHEAD [Ref. IMC Sec. 5-9-515]

A.	Wood doors shall have panels a minimum of 5/16 inch in thickness with the locking hardware being attached to the support framing.

B.	Aluminum doors shall be a minimum thickness of 0.0215 inches and riveted together a minimum of 18 inches on center along the outside seams. There shall be a full width horizontal beam attached to the main door structure which shall meet the pilot, or pedestrian access, door framing within three inches of the strike area of the pilot or pedestrian access door.

C.	Fiberglass doors shall have panels a minimum density of six ounces per square foot from the bottom of the door to a height of seven feet. Panels above seven feet and panels in residential structures shall have a density not less than five ounces per square foot.

D.	Doors utilizing a cylinder lock shall have a minimum five-pin tumbler operation with the locking bar or bolt extending into the receiving guide a minimum of one inch.

E.	Doors that exceed 16 feet in width shall have two lock receiving points; or, if the door does not exceed 19 feet, a single bolt may be used if placed in the center of the door with the locking point located either at the floor or door frame header; or, torsion spring counterbalance-type hardware may be used.

F.	Doors secured by electrical operation shall have a keyed-switch to open the door when in a closed position, or by a signal locking device.

G.	Doors with slide bolt assemblies shall have frames a minimum of 0.120 inches in thickness, with a minimum bolt diameter of 1/2 inch and protrude at least one and one-half inches into the receiving guide. A bolt diameter of 3/8 inch may be used in a residential building. The slide bolt shall be attached to the door with non-removable bolts from the outside. Rivets shall not be used to attach slide bolt assemblies.

(*)  || STANDARDS FOR EXTERIOR LADDERS [Ref. IMC Sec. 5-9-517]

[P] Exterior mounted ladders are prohibited except:

A.	Ladders with a minimum 1/8 inch thick steel plate, securely attached to the ladder edge on each side and extending to within two inches of the wall for a height of ten feet above ground level. A door or cover shall be securely attached to the front of the ladder and be constructed of a minimum 1/8-inch steel, extending from ground level to at least ten feet high. The ladder door shall have nonremovable hinge pins and be locked tight against the side wall by a locking mechanism with a minimum five pin tumbler operation, and attached with nonremovable bolts from the exterior; or

B.   Ladders beginning a height of ten feet above ground.

{Ref. plans, elevations and applicable notes and/or details-      }

(*)  || EMERGENCY ACCESS [Ref. IMC Sec. 5-9-519]

Unmanned mechanical parking type gates shall provide for police emergency access utilizing an approved key switch device and designed as follows:

A.	[P] A control pedestal consisting of a metal post/pipe shall be installed at a height of 42 inches and a minimum of 15 feet from the entry/exit gate. It shall be located on the driver's side of the road or driveway and accessible in such a manner as to not require a person to exit their vehicle to reach it; nor to require any back-up movements in order to enter/exit the gate.

B.	[P] A control housing consisting of a heavy gauge metal, vandal and weather resistant square or rectangular housing which shall be installed on the top of the control pedestal. Keyswitch is to be mounted on the side facing the roadway.

{Ref. plans, elevations and applicable notes and/or details-      }