CITY OF IRVINE

STANDARD NON-RESIDENTIAL SECURITY CODE PROVISIONS

[Version 2.0 applies to applications made on or after 1/1/11]

This document shall be completed by the design professional of record. The completed document shall be incorporated, in its entirety, along with the City of Irvine Standard Security Code Plan Requirements and Definitions into the plans submitted for approval prior to permit issuance. This document is in 12 point font and may not be reduced in size prior to incorporation.

INSTRUCTION: (1) Those provisions preceded by an asterisk (*) shall be completed if applicable and an “A” shall be inserted in the space preceding the provision; if not applicable, an “N/A” shall be inserted. (2)Those provisions preceded by a [P] shall be depicted in the plans via notes, details, plan and/or elevation views in a manner that clearly demonstrates compliance to the requirement. Such depictions shall be crossed referenced within the brackets { } provided or note shall be completed as otherwise instructed.

KEYING REQUIREMENTS [Ref. IMC Sec. 5-9-511]

Upon occupancy by the owner or proprietor, each single unit shall have locks using combinations which are interchange free from locks used in all other proprietorships or similar distinct occupancies.

(*)  || STANDARDS FOR LOUVERED WINDOWS [Ref. IMC Sec. 5-9-514]

[P] Louvered windows shall not be utilized if any portion of it is within eight feet vertically or six feet horizontally from any exterior accessible surface or any adjoining roof, balcony, landing, stair tread, platform or similar structure.

{Ref. elevation views, window schedule-      }

(*)  || STANDARDS FOR GARAGE DOORS: ROLLING OVERHEAD, SOLID OVERHEAD [Ref. IMC Sec. 5-9-515]

A.	[P] Wood doors shall have panels a minimum of 5/16 inch in thickness with the locking hardware being attached to the support framing. {ref. plans and/or door schedules or note: Not Applicable-      }

B.	[P] Aluminum doors shall be a minimum thickness of 0.0215 inches and riveted together a minimum of 18 inches on center along the outside seams. There shall be a full width horizontal beam attached to the main door structure which shall meet the pilot, or pedestrian access, door framing within three inches of the strike area of the pilot or pedestrian access door. {ref. plans and/or door schedules or note: Not Applicable-      }

C.	[P] Fiberglass doors shall have panels a minimum density of six ounces per square foot from the bottom of the door to a height of seven feet. Panels above seven feet shall have a density not less than five ounces per square foot. {ref. plans and/or door schedules or note: Not Applicable-      }

D.	Doors utilizing a cylinder lock shall have a minimum five-pin tumbler operation with the locking bar or bolt extending into the receiving guide a minimum of one inch.

E.	Doors that exceed 16 feet in width shall have two lock receiving points; or, if the door does not exceed 19 feet, a single bolt may be used if placed in the center of the door with the locking point located either at the floor or door frame header; or, torsion spring counterbalance-type hardware may be used.

F.	[P] Doors secured by electrical operation shall have a keyed-switch to open the door when in a closed position, or by a signal locking device. {ref. plans and applicable notes and/or details or note: Not Applicable-      }

G.	Doors with slide bolt assemblies shall have frames a minimum of 0.120 inches in thickness, with a minimum bolt diameter of 1/2 inch and protrude at least one and one-half inches into the receiving guide. A bolt diameter of 3/8 inch may be used in a residential building. The slide bolt shall be attached to the door with non-removable bolts from the outside. Rivets shall not be used to attach slide bolt assemblies.

STANDARDS FOR EXTERIOR DOORS & OPENININGS [Ref. IMC Sec. 5-9-517]

A.	Exterior glass doors, wood or metal doors with glass panels, solid wood or metal doors and all entrance doors to individual office suites shall be constructed or protected as follows:

1.	[P] Wood doors shall be of solid core construction with a minimum thickness of 1-3/4 inches. Wood panel doors with panels less than one inch thick shall be covered on the inside with a minimum 16 U.S. gauge sheet steel or its equivalent, which is to be attached with screws on minimum six-inch centers. Hollow steel doors shall be of a minimum 16 U.S. gauge and have sufficient reinforcement to maintain the designated thickness of the door when any locking device is installed; such reinforcement being able to restrict collapsing of the door around any locking device.

{ref. plans and/or door and window schedules-      }

2.   	[P] Except when double cylinder deadbolts are utilized, any glazing utilized within 40 inches of any door locking mechanism shall be constructed or protected as follows:

a.   Fully tempered glass or rated burglary resistant glazing; or

b.   Iron or steel grills of at least 1/8-inch material with a minimum two-inch mesh secured on the inside of the glazing may be utilized; or

c.   The glazing shall be covered with iron bars of at least 1/2 inch round or one-inch by 1/4-inch flat steel material, spaced not more than five inches apart, secured on the inside of the glazing.

d.   Items b. and c., above, shall not interfere with the operation of opening windows if such windows are required to be openable by the California Building Code.

{ref. plans and/or door and window schedules-      }

B.     All swinging exterior wood and steel doors shall be equipped as follows:

1.	A single or double door shall be equipped with a double or single cylinder deadbolt. The bolt shall have a minimum projection of one inch and be constructed so as to repel a cutting tool attack. The deadbolt shall have an embedment of at least 3/4 inch into the strike receiving the projected bolt. The cylinder shall have a cylinder guard, a minimum of five-pin tumblers, and shall be connected to the inner portion of the lock by connecting screws of at least 1/4 inch in diameter. The provisions of the preceding paragraph do not apply where (1) panic hardware is required, or (2) an equivalent device is approved by the enforcing authority.

2.     Double doors shall be equipped as follows:

a.  The inactive leaf of double door(s) shall be equipped with metal flush bolts having a minimum embedment of 5/8 inch into the head and threshold of the doorframe.

b.  Double doors shall have an astragal constructed of steel a minimum of 0.125 inch thick, which will cover the opening between the doors. The astragal shall be a minimum of two inches wide, and extend a minimum of one inch beyond the edge of the door to which it is attached. The astragal shall be attached to the outside of the active door by means of welding or with non removable bolts spaced apart on not more than ten inches centers. (The door to which such an astragal is attached must be determined by the fire safety codes adopted by the enforcing authority.)

C.     Aluminum frame swinging doors shall be equipped as follows:

1.   The jamb on all aluminum frame swinging doors shall be so constructed or protected to withstand 1,600 pounds of pressure in both a vertical distance of three inches and a horizontal distance of one inch each side of the strike, so as to prevent violation of the strike.

2.   A single or double door shall be equipped with a double cylinder deadbolt with a bolt projection exceeding one inch or a hook-shaped or expanding deadbolt that engages the strike sufficiently to prevent spreading. The deadbolt lock shall have a minimum of five-pin tumblers and a cylinder guard.

D.	Panic hardware, whenever required by the Building Code shall be installed as follows:

1.   Panic hardware shall contain a minimum of two locking points on each

door; or

2.  On single doors, panic hardware may have one locking point, which is not to be located at either the top or bottom rails of the doorframe. The door shall have an astragal constructed of steel 0.125 inch thick, which shall be attached with nonremovable bolts to the outside of the door. The astragal shall extend a minimum of six inches vertically above and below the latch of the panic hardware. The astragal shall be a minimum of two inches wide and extend a minimum of one inch beyond the edge of the door to which it is attached.

3.	Double doors containing panic hardware shall have an astragal attached to the doors at their meeting point, which will close the opening between them, but not interfere with the operation of either door.

E.   	Horizontal sliding doors shall be equipped with a metal guide track at top and bottom, and a cylinder lock and/or padlock with a hardened steel shackle which locks at both heel and toe, and a minimum five-pin tumbler operation with nonremovable key when in an unlocked position. The bottom track shall be so designed that the door cannot be lifted from the track when the door is in a locked position.

(*)  || STANDARDS FOR ROOF OPENINGS [Ref. IMC Sec. 5-9-517]

[P] Roof openings shall be protected as follows if the roof is accessible via an exterior ladder or the roof is less than 20 feet from ground level or if any portion of it is within 12 feet vertically or six feet horizontally from any exterior accessible surface or any adjoining roof, balcony, landing, stair tread or similar structure:

A.   All skylights on the roof of any building used for business purposes shall be provided with:

1.  Rated burglary-resistant glazing; or

2.  Iron bars of at least one-half inch round or one by 1/4 inch flat steel material under the skylight and securely fastened; or

3.  A steel grill of at least 1/8 inch material with a maximum two-inch mesh under the skylight and securely fastened.

B.  All hatchway openings on the roof of any building or premises used for business purposes shall be secured as follows:

1.  If the hatchway is of wooden material, it shall be covered on the inside with at least 16 U.S. gauge sheet metal, or its equivalent, attached with screws.

2.  The hatchway shall be secured from the inside with a slide bar or slide

bolts.

3.  Outside hinges on all hatchway openings shall be provided with nonremovable pins when using pin-type hinges.

{ref. plans and details-      }

(*)  || STANDARDS FOR EXTERIOR LADDERS [Ref. IMC Sec. 5-9-517]

[P] Exterior mounted ladders are prohibited except:

A.	Ladders with a minimum 1/8 inch thick steel plate, securely attached to the ladder edge on each side and extending to within two inches of the wall for a height of ten feet above ground level. A door or cover shall be securely attached to the front of the ladder and be constructed of a minimum 1/8-inch steel, extending from ground level to at least ten feet high. The ladder door shall have nonremovable hinge pins and be locked tight against the side wall by a locking mechanism with a minimum five pin tumbler operation, and attached with nonremovable bolts from the exterior; or

B.  Ladders beginning a height of ten feet above ground.

{Ref. plans, elevations and applicable notes and/or details-     }

EXTERIOR PHONE PANELS ARE PROHIBITED [Ref. IMC Sec. 5-9-517]

STANDARDS FOR LIGHTING [Ref. IMC Sec. 5-9-517]

Note: Performance standards are contained herein for reference. Compliance shall be demonstrated in photometric study preceding plan check approval.

Buildings, open parking lots, walkways, and accesses thereto shall conform to the following light standards and be arranged in such a way so as to conform to California Green Building Standards Code section 5.106.5.2 and Zoning Code Section 3-16-1 which require that direct rays be confined to the site and that adjoining properties are protected from glare such that at 15 feet beyond site boundaries illumination is less than 0.01 horizontal footcandles.

A.	[P] All types of exterior doors shall be illuminated during the hours of darkness, with a minimum maintained one foot-candle of light, measured within a five-foot radius on each side of the door at ground level. The light source shall be controlled by a photocell device or a timeclock with an astronomic clock feature and capable of operating during a power outage. {Ref. plans, elevations and applicable notes and/or details-      }

B.	Recessed areas of buildings or fences, which have a minimum depth of two feet, a minimum height of five feet, and do not exceed six feet in width and are capable of human concealment, shall be illuminated with a minimum maintained 0.25 foot-candles of light at ground level during the hours of darkness. This requirement applies to defined recessed areas which are within six feet of the edge of a designated walking surface with an unobstructed pathway to it, not hindered by walls or hedge row landscaping a minimum of two feet in height.

C.	Stairways shall be illuminated with a minimum maintained one foot-candle of light on all landings and stair treads, during the hours of operation, including one hour thereafter.

D.	All interior or exterior corridors, passageways and walkways in any hotel, motel or inn shall be illuminated at all times with a minimum maintained one foot-candle of light on the walking surface.

E.	All exterior pedestrian walkways, interior common corridors, and open parking lots shall be illuminated with a minimum maintained one foot-candle of light on the walking or driving surface during the hours of operation and one hour thereafter.

F.	[P] For buildings required to have two or more exits, lighting for landings shall be on an emergency power system consisting of storage batteries or an onsite generator capable of providing power for 90 minutes, installed as required by California Building Code Section 1006.3. {Ref. plans, elevations and applicable notes and/or details or note: This provision is not applicable-      }

G.	The light source utilized to comply with this section to meet parking and drive surface lighting shall have a rated average bulb life of not less than 10,000 hours.

H.	[P] Accessible luminaires utilized to meet the requirements of this section have vandal resistant light fixtures and be not less than three feet in height from ground level when used to illuminate walkways and a minimum of eight feet in height from ground level when illuminating surfaces associated with vehicles. Light fixtures shall be deemed accessible if mounted within fifteen feet vertically or six feet horizontally from any accessible surface or any adjoining roof, balcony, landing, stair tread, platform or similar structure. {Ref. plans, elevations and applicable notes and/or details or note: This provision is not applicable-     }

I.	[P] See plan sheet {Ref. plans or note: This provision is not applicable-     }

showing buildings, parking area, walkways, detailed landscaping and a point-by-point photometric calculation of the required light levels. Note: Foot-candles are measured on a horizontal plane and conform to a uniformity ratio of 4:1 average/minimum. Landscaping shall be planted and maintained in a manner so as not to obscure required light levels.

STANDARDS FOR ADDRESSING [Ref. IMC Sec. 5-9-517]

[P] Buildings shall display a street address number conforming to the following specifications:

A.  Numerals shall be mounted on the wall, no higher than 30 feet, and face the street on which the building is addressed.  Numerals are to be clearly visible from this same street and not obscured by building landscaping at full maturity.  Addressing shall be of a color contrasting to the background to which they are affixed. Method of attachment shall not include the use of two-sided tape or any material not resistant to weather conditions. {Ref. plans, elevations and applicable notes and/or details-     }

B.  Where distance or intervening obstructions impair visibility from the street, addressing shall be mounted on all buildings so as to be visible from drive aisles and walkways internal to the site, and each such address, or an encompassing range of addresses, shall be displayed on monument signs visible from each site entrance from all approaching directions.  In such cases, directional wayfinding signs shall be provided per item E. below. {Ref. plans, elevations and applicable notes and/or details or note: This provision is not applicable-     }

C. Numerals shall be no less than 12 inches in height and shall be in a Sans Serif font with a stroke weight of medium to bold, or an approved equivalent font which is clearly legible, and illuminated during the hours of darkness using a light source provided with an uninterruptible A.C. power source or controlled only by a photoelectric device, which may be the common area site lighting. {Ref. plans, elevations and applicable notes and/or details or note: This provision is not applicable-     }

D. The rear doors of all buildings shall have address numbers not less than six inches in height, using a Sans Serif font with a stroke weight of medium to bold, or an approved equivalent font which is clearly legible, and be of a color contrasting to the background to which they are affixed.  Method of attachment shall not include the use of two-sided tape or any material not resistant to weather conditions {Ref. plans, elevations and applicable notes and/or details or note: This provision is not applicable-     }

E.	For sites having multiple buildings for which addressing mounted on building is not clearly visible from the street, or for which drive aisles diverge from a site entrance in a manner such that the direct route to each building is not obvious, vehicle directional signs shall be provided.  Vehicle direction signage from the point of site entry to each building entrance shall display building addresses or unit number range, and be located at all turning points along the route to a building entrance. Signs shall be no less than two feet from ground level and not obstructed by landscaping at full maturity or parked cars.  Numerals shall be at least 3 inches in height using a Sans Serif font with a stroke weight of medium to bold, or an approved equivalent font which is clearly legible. {Ref. plans, elevations and applicable notes and/or details or note: This provision is not applicable-     }

F.	Buildings, except parking strutures, with a total square footage of at least 10,000 square feet shall have rooftop numbers placed parallel to the addressed street, screened from public view and only visible from the air. The numerals are to be white, block lettered, constructed of weather resistant material, and placed against a black background. Address numbers are to be a minimum of four feet in height and 18 inches wide. When more than one street address is assigned to a building, the beginning and ending address numbers are to be placed on the rooftop, at opposite ends of the building, reflecting the approximate location of these addresses.

Exceptions: 1) 	For buildings having white roofing, black lettering shall be used in lieu of white lettering.

2) Buildings providing addressing for a helipad as specified in                the California Building Code.

{Ref. plans, elevations and applicable notes and/or details or note: This provision is not applicable-     }

(*)  || STANDARDS FOR ELEVATOR [Ref. IMC Sec. 5-9-517]

Elevators shall be designed as follows:

A.  Elevator cabs, the interiors of which are not completely visible when the door is open from a point centered on and 36 inches away from the door, shall have shatter resistant mirrors or other equally reflective material so placed as to make visible the entire elevator cab from this point. The elevator cab shall be illuminated at all times with a minimum maintained two foot-candles of light at floor level. {Ref. plans, elevations and applicable notes and/or details or note: This provision is not applicable as interior is completely visible per specification above-      }

B.  Elevator emergency stop buttons shall be so installed and connected as to activate the elevator alarm when utilized.

(*)  || EMERGENCY ACCESS [Ref. IMC Sec. 5-9-519]

Private roads and parking areas or structures controlled by unmanned mechanical parking type gates shall provide for police emergency access utilizing an approved key switch device and designed as follows:

A.	[P] A control pedestal consisting of a metal post/pipe shall be installed at a height of 42 inches and a minimum of 15 feet from the entry/exit gate. It shall be located on the driver's side of the road or driveway and accessible in such a manner as to not require a person to exit their vehicle to reach it; nor to require any back-up movements in order to enter/exit the gate.

B.	[P] A control housing consisting of a heavy gauge metal, vandal and weather resistant square or rectangular housing which shall be installed on the top of the control pedestal. Keyswitch is to be mounted on the side facing the roadway.

{Ref. plans, elevations and applicable notes and/or details-      }